## Slide 1
Digital Filters Design: Pole Zero Placement
carmine.clemente@strath.ac.uk
Digital filters

## Slide 2: Introduction
At the discrete LTI analysis stage we have learned how to derive the frequency response of a system from its Zero-Pole diagram;
A zero will cause a zero of the magnitude response in the corresponding point, while a pole will cause a peak;
The closer the poles to the unit circle are the higher is the peak, while closer is the zero to the unit circle the sharper is the decrease of magnitude;

## Slide 3: Introduction
We can use our knowledge to strategically decide where to put poles and zeros and design our desired magnitude response of a digital filter!

## Slide 4: Zero Pole placement: design consideration
Remember: in order to have real valued coefficients for our filter we need to have real poles and zeros or occurring in complex conjugate pairs.
Real(z)
Im(z)
z-plane
x
o
o
o
o
x
x

## Slide 5: Zero Pole placement: Example 1
Let’s design a filter using zero-pole placement and derive its difference equation using the following specifications:
  Complete signal rejection at dc and 250Hz
  A narrow passband centered at 125Hz
  A 3 dB bandwidth of 10 Hz;
  The filter should operate on signal sampled at a sampling frequency of 500 Hz;

## Slide 6: Zero Pole placement: Example 1
Real(z)
Im(z)
z-plane
o
  Complete signal rejection at dc and 250Hz
o
One zero in 0
One zero in
To get complete signal rejection we put them on the unit circle

## Slide 7: Zero Pole placement: Example 1
Real(z)
Im(z)
z-plane
o
  A narrow passband centered at 125Hz
o
Complex conjugate poles in
Using complex conjugate poles ensures real coefficients.
x
x

## Slide 8: Zero Pole placement: Example 1
  A 3 dB bandwidth of 10 Hz;
The radius is determined by the desired bandwidth.
An approximate approximation between and bandwidthfor is given by:
In our case
Real(z)
Im(z)
z-plane
o
o
x
x

## Slide 9: Zero Pole placement: Example 1
  By inspection we can now write the system function
Real(z)
Im(z)
z-plane
o
o
x
x

## Slide 10: Zero Pole placement: Example 1
And from we can get the linear difference equation

## Slide 11: Zero Pole placement: Example 2
Let’s design a filter using zero-pole placement to obtain the coefficients of a notch filter with the following specifications:
  Notch frequency 50Hz;
  3 dB width of notch 5Hz;
  Sampling frequency 500 Hz;

## Slide 12: Zero Pole placement: Example 2
Real(z)
Im(z)
z-plane
o
  Notch frequency 50Hz
o
Pair of complex zeros at 50Hz,

## Slide 13: Zero Pole placement: Example 2
Real(z)
Im(z)
z-plane
o
  3 dB width of notch 5Hz;
o
To achieve this we can put a pair of complex conjugate poles at the same frequency but with radius.
The width of the notch is determined by the location of the poles
As in the previous example
we are looking for a 10 Hz bandwidth, thus
x
x

## Slide 14: Zero Pole placement: Example 2
Real(z)
Im(z)
z-plane
o
  By inspection we can now write the system function
o
x
x
0

## Slide 15: Zero Pole placement: Example 2
And we can get the linear difference equation of the filter as:
0