## Slide 1
DSP Principles 2023/2024
EE469/EE669/EE869/EE969
carmine.clemente@strath.ac.uk
Module Introduction

## Slide 2: Academic Team
Dr Carmine Clemente – Reader
Director of Sensor Signal Processing & Security Labs
Area of expertise: Radar signal processing.
Dr Christos Ilioudis – Research Fellow
Holder of the Royal Academy of Engineering IC Security Fellowship
Area of expertise: Radar signal processing.
Dr Jaime Zabalza – Lecturer – Chancellor’s Fellow
Area of expertise: Artificial Intelligence, Hyperspectral Imaging.

## Slide 3: Teaching Assistants
James McCleary
Elmergue Germano
Finlay Rollo
Hemanga Banerjee

## Slide 4: DSP in EEE at Strathclyde
Inst EE
Energy & Environment
CMP
Mems&Photonics
CUE
Ultrasonics
CIDCOM
Comms
Inst (SSC) Sensors, Signals and
Communications
CeSIP
S&I Proc

## Slide 5: DSP going on in CeSIP
ML&DL/SNN
Radar, Remote Sensing & Security
Biomedical Imaging
Speech, Image and Video Processing
Biosignals ECG, EMG, Speech
Dr Clemente
Dr Di Caterina
Dr Iloudis
Dr Kirkland
Machine Learning & Neuromorphic Sensor Processing Lab
Biosignal and Biomedical Signal Processing Lab
Sensor Signal Processing & Security Lab

## Slide 6: What is DSP
DSP is an enabling science
Real DSP solutions work hand-in-hand with technological developments
  DSP algorithms are integrally aligned to DSP architectures (technologies)
Proper DSP designs allow us to produce smaller, cheaper, smarter, and more flexible TOTAL solutions for a diverse range of applications

## Slide 7: Where do we use DSP?
Green
Robotics
Full immersion
Health
Security & Remote Sensing
IOT & Autonomous Systems
These are just some of the areas in which DSP is used… try to count how many functions and apps do DSP on your smartphone.

## Slide 8: Where do we use DSP?
Machine Learning & Deep Learning Neural Networks
SMART Mobile Phones and Wireless Technology
Digital Cameras and Digital Art Technologies
Digital Video recorders (DVR) and Network Video Recorders (NVR)
Speech , audio and music processing
Broadband and Wireless Telecommunication Networks
Radar and Sonar Data processing
Navigation and Tracking Systems
Video Surveillance
Biologically Inspired electronic systems
Seismic, Geophysical and Astronomical Data Interpretation
Biomedical Signal Processing and implanted medical devices
Chemical Data Processing
Virtual Reality, Games, 3-dimensional modelling and Digital Holography
Financial Data Processing
Smart Meters and the Smart Grid
Intelligent Power Supplies
Energy Scavenging devices
Autonomous Systems
Internet of Things (IOT)
… etc

## Slide 9: Aim & Learning Objectives
Understand:
  Core Maths
  Fundamental Principles
  Algorithms
  Applications
Use:
  Design tools
  Design, analyse and simulate
  Matlab to implement basic DSP algorithms
Pre-requisites:
  a basic understanding of continuous linear systems
  an eagerness to learn
  a basic knowledge of complex numbers

## Slide 10: Syllabus Overview
Block 5: Applications:
Time Frequency Representation of Signals
Speech Processing
Radar Signal Processing principles
Matched filtering in radar/sonar
Range-Doppler representation
Micro-Doppler analysis using time-frequency distributions
Block 2: Signal Transforms:
Discrete Fourier Series -- DFT
Z-Transform- Discrete System Analysis
DTFT- DFT Resolution, Spectral Leakage & Scallop Loss
Acquisition, Windowing
Frequency Sampling, DFT
DFT Evaluation -- DFT Matrix Method & FFT
Block 4: Digital Filters
FIR , IIR
Linear Phase Digital Filters
Digital Filter Design
Efficient Multirate Digital Filters
Block 3: Fundamental Applications
Time Sampling Nyquist Sampling- Aliasing
Signal Reconstruction (DAC)
Decimation and Interpolation
Block 1: Signals & LTI Discrete Systems:
Discrete Signals and Systems
Convolution/Correlation
Cyclic Convolution and Correlation
Overlap Add and Overlap Save methods
Semester 1
Semester 2

## Slide 11: Available material through myplace
Matlab on a ramp short course – compulsory by week 2
Lecture notes
Lectures slides
Tutorial questions
Matlab lab tasks
Reference Reading material

## Slide 12: Reference Material
“Digital Signal Processing:- Principles, Algorithms and Applications” 3rd edition by John Proakis and Dimitris Manolakis, Prentice Hall, ISBN 0-13-394338-9
“Discrete-Time Signal Processing” 2nd edition by Alan Oppenheim and Ronald Schafer, Prentice Hall Inc, ISBN 0-13-754920-2
“Digital Signal Processing: A Computer Based Appoach” 4th Edition Sanjit Mitra, McGraw Hill, ISBN: 978-007-128946-7 , 2011
“Digital Signal Processing” by Monson Hayes, Schaum’s Outline Series, ISBN 0-07-027389-8
“DSP First – A Multimedia Approach” by Mclellan-Schafer – Yoder, Prentice Hall, ISBN : 0-13-243171-8
“Signals and Systems” , Baraniuk et al – available on myplace
Many internet sites such as:
http://www.dspguide.com/ (a free DSP book)

## Slide 13: ASSESSMENT EE469
Laboratory (20% - CA1 &CA2)
Matlab on a ramp – compulsory to unlock the matlab grader tasks – weeks 0-2
Set of Matlab tasks to be released before the labs in weeks 2-4-6-8 of each semester (2.5% each). A total of 8 tasks will be released – 4 per semester and graded through matlab grader.
Tasks to be completed by the end of semesters 1 and 2
Theory (30% - CA3 & CA4)
In week 9 of each semester there will be a test on the theoretical content of the module. Each test will be worth up to 15% of the final mark.
The test will be composed of open and closed solution questions.
EXAM (50%)
End of year exam, 3 questions out of 5offered.

## Slide 14: ASSESSMENT EE669
Laboratory (30% - CA1)
Matlab on a ramp – compulsory to unlock the matlab grader tasks – weeks 0-2
Set of Matlab tasks to be released before the labs in weeks 2-4-6-8 (7.5% each). A total of 4 tasks will be released and graded through matlab grader.
Tasks to be completed by the end of semester 1
Theory (35% - CA3)
In week 9 of each there will be a test on the theoretical content of the module.
The test will be composed of open and closed solution questions.
DSP topic (35%-CA5)
Each student selects a DSP topic and is asked to produce a short video presentation (10 minutes) about the topic. (28%)
Additionally, each student is asked to watch 2 other videos (assigned randomly) and to engage via a forum with the author in an asynchronous Q&A session. (7%)- Subject to cohort numbers
Submission end of Semester 1.

## Slide 15: ASSESSMENT EE869
Laboratory (40% - CA1)
Matlab on a ramp – compulsory to unlock the matlab grader tasks – weeks 0-2
Set of Matlab tasks to be released before the labs in weeks 2-4-6-8 (10% each). A total of 4 tasks will be released and graded through matlab grader.
Tasks to be completed by the end the semester
Theory (20% - CA3)
In week 9 of each there will be a test on the theoretical content of the module.
The test will be composed of open and closed solution questions.
DSP topic (40%-CA5)
Each student selects a DSP topic and is asked to produce a short video presentation (10 minutes) about the topic. (30%)
Additionally, each student is asked to watch 2 other videos (assigned randomly) and to engage via a forum with the author in an asynchronous Q&A session. (5%)
By the end of semester 1 the topics is assigned and students are asked to submit a short abstract (1-2 pages). (5%)
Submission end of Semester 2.

## Slide 16: ASSESSMENT EE969
Laboratory (20% - CA1 &CA2)
Matlab on a ramp – compulsory to unlock the matlab grader tasks – weeks 0-2
Set of Matlab tasks to be released before the labs in weeks 2-4-6-8 of each semester (2.5% each). A total of 8 tasks will be released – 4 per semester and graded through matlab grader.
Tasks to be completed by the end of semesters 1 and 2
Theory (30% - CA3 & CA4)
In week 9 of each semester there will be a test on the theoretical content of the module. Each test will be worth up to 15% of the final mark.
The test will be composed of open and closed solution questions.
DSP Topic (10%- CA5)
Each student selects a DSP topic and is asked to produce a short video presentation (10 minutes) about the topic (in the past they were asked to write a conference paper). (7%)
Additionally, each student is asked to watch 2 other videos (assigned randomly) and to engage via a forum with the author in an asynchronous Q&A session. (3%)
Submission at the end of Semester 2
EXAM (40%)
End of year exam, 3 questions out of 5 offered.

## Slide 17: Delivery method
Lectures
  Live lectures
Tutorials
Laboratories
  Matlab tasks released on the lab day through myplace;
  Matlab tasks to be completed and submitted asynchronously via matlab grader.

## Slide 18: Interacting with the teaching team
Use the Forums on myplace
Contact us via e-mail.
  carmine.clemente@strath.ac.uk
  j.zabalza@strath.ac.uk
  c.ilioudis@strath.ac.uk

## Slide 19: Questions?

## Slide 20
Introduction to DSP
carmine.clemente@strath.ac.uk
Intro to DSP

## Slide 21: Historical notes
Until the early 1950s the extraction of information from signals was performed exclusively with analog systems implemented with electronic circuits or even mechanical devices;
With the growing availability and more general capabilities of digital computers the use of DSP became more and more diffused until today with the vast majority of signals processed digitally;
From this…
Analog
to this
Digital

## Slide 22: Introduction to DSP
DSP represents an enabling technology with solid history and great future thanks to the synergy of theoretical development, sophisticated applications and constantly emerging new hardware.
We have already listed a broad set of application domains in which DSP plays a fundamental role, but to give you an idea let us analyse an example:
ADAS System
  Electronics systems on a modern car:

## Slide 23: Introduction to DSP
Signal processing deals with the representation, transformation, and manipulation of signals and the information the signals contain;
Examples are separating two signals (e.g. useful and interferer) or estimate a signal parameter (e.g. time difference or angle of arrival);
When we talk about Digital Signal Processing and/or Discrete time signal processing we generally refer to signals whose time variable is the independent variable, however, without loss of generality the discrete independent variable could be anything (e.g. space, angle);
Amplitude [V]
Time [s]
Income [$]
Sales [#]

## Slide 24: Basic Elements of a DSP System
Most of the signals encountered in science and engineering are of analog nature, indeed they are functions of a continuous variable (time, space, etc) and can take values in a continuous range.
These signals can be processed using an analog signal processor:
Analog signal processor
Analog Input
Analog Output

## Slide 25: Basic Elements of a DSP System
DSP provides an alternative to the analog signal processor by processing the information digitally;
Introduces the need for an interface between the analog and the digital world in input and (not always) in output.
The analog to digital converter (A/D) is the required interface to convert the input signal in a digital version, while the Digital to analog converter (D/A) is used to convert the processed output in analog form;
The Digital Signal Processor can be a large programmable computer, a dedicated programmable chip or a hardwired digital processor.
Digital Signal Processor
Digital Input signal
Analog Output
A/D converter
D/A converter
Digital Output signal
Analog Input

## Slide 26: Advantages of DSP
Flexibility: operations can be easily reconfigured by changing the program (not easy in an analog system);
Accuracy control: analog systems include tolerance that need to be taken into account, digital systems provide higher level of control on the accuracy;
Storage and portability: Digital signals are much easier to store on memory support and to port on other media;
Processing complexity: using software it is possible to implement very complex operations on signals that would have required extremely complex hardware if performed in analog;
Cost: thanks to the general purpose of many DSP processors and the lack of the design of dedicated HW, the cost of DSP system is significantly less of an analog processor.

## Slide 27: Drawback of DSP
A/D conversion speed: the main drawback is the need to have A/D converters fast enough to handle signals with rapidly changing characteristics, meaning that for signals with large bandwidths the cost explodes or analog systems must be used;
However technology is improving year after year making A/D converter capabilities always better.

## Slide 28
Complex Exponential
carmine.clemente@strath.ac.uk
Complex Exponential

## Slide 29: The Complex Exponential
The complex Exponential plays a key role in DSP, as you will see, we will use the complex exponential in a number of DSP tools and techniques throughout the course (i.e. DFS, DFT, FFT, frequency analysis);
The complex exponential is composed by a sine and a cosine:

## Slide 30: The Complex Exponential
How do we get to this definition?
Lets say we want a function so that:
and that at the same time a condition on its derivative is satisfied too
The complex exponential is the only function satisfying this relationship
Indeed the derivative is:
This is called Euler’s Formula

## Slide 31: The Complex Exponential
To demonstrate the use of the exponential notation, prove (as an exercise) the following form of the Law of Exponents:
To prove this expand the right-hand side and use the trigonometric identities:
2. Also show that
To prove it just write the right hand side of both equations in terms of cosine and sine
This is called De Moivre’s Theorem

## Slide 32: The Complex Exponential
Now we want to find out specific values of the complex exponential (e.g );
Recall that the relationship between cartesian coordinates and polar coordinates of a point is:
Making use of Euler’s formula, we can express polar representation in the following manner:
  Where
Is the Magnitude
Is the Phase

## Slide 33: The Complex plane
Imaginary axis
Real axis

## Slide 34: Complex Exponential Example
Let us consider with
Therefore
Note also that, due to the periodicity of sine and cosine (i.e. both have fundamental period of 2π) , if z = rejθ, then we also have
Thus, in our last example,
Exercise: Sketch these on the complex plane to convince yourself

## Slide 35: Complex Plane Example
Express points A, B, C and D as general complex numbers in Polar and Cartesian Form if the magnitude of all these points is 1.
A
D
C
B

## Slide 36
Signal Classification
carmine.clemente@strath.ac.uk
Signal Classification and ADC

## Slide 37: Signal Classification
The term signal is generally applied to something that conveys information;
Signals can be represented in may ways, however information is conveyed via some sort of pattern or variation;
Signals are generally represented as mathematical functions of one or more independent variable (usually time);
Continuous-time signals are defined along a continuum time and are thus represented by a continuous independent variable;
Discrete-time signals are defined at discrete times, thus the independent variable has discrete values;
Discrete-time signals are represented as a sequence of numbers;
Signals such as images or speech can be represented both as continuous and discrete, and under certain conditions the two representations are equivalent.

## Slide 38: Continuous Time Signals
An example of a Continuous Time – Continuous Amplitude signal on the time interval t = [0,1];
and an example of Continuous Time- Discrete Amplitude signal on the time interval t = [0,1] and Quantized with an interval of Q = 0.1.

## Slide 39: Discrete Time Signals
An example of a Discrete Time – Continuous Amplitude signal sampled at 50 Hz on the interval n =[0,50];
and an example of Discrete Time- Discrete Amplitude signal sampled at 50 Hz on the interval n=[0,50] and Quantized with an interval of Q = 0.1.

## Slide 40: Fundamental Discrete Signals
exponential
complex exponential
damped complex exponential
e(a+jw)t= eatejwt=eat[cos(wt)+jsin(wt)]

## Slide 41: Fundamental Signals
Note:
Discrete Time Unit Impulse (sampling/sifting) function
Like the RELU function in Deep Learning
Example: Given functions & then
is the function switched on at
while
is the function switched on at added to the function switched on at time .

## Slide 42: Fundamental Discrete Signals
All of these continuous signals may be converted to discrete sampled (DTCA) signals by simply letting t=nT where T is the sampling interval and
is the sampling frequency in Hz or samples per second.
such that becomes
The square brackets means the sampling interval T is implied

## Slide 43: Digital freq./fundamental Period
A sampled version of  a 50 Hz sinusoid using a sampling frequency of 400 Hz (i.e. T=1/400 sec) may be written as
where is the digital frequency.
One period of this discrete sinusoid, with frequency , corresponding to
  is
Note:
  Period of is where
   for some integer .
  So for the above example for . This is the fundamental period of

## Slide 44: Discrete Complex Exponential – Exercises
exponential
complex exponential
damped complex exponential
Find an expression for for each of these for and and and . Make a Matlab plot of these.
Compute the digital frequency and the fundamental period for the complex exponential.

## Slide 45: Operations on Signal

## Slide 46: Operations on Signal

## Slide 47: Operations on Signal

## Slide 48: Energy and Power
Energy and Power of a discrete signal are important measures of this type of signals
For aperiodic signals it is possible to define the energy of a discrete signal as
Instead, for periodic signals, the energy is infinite, so we need to compute its power
the power is the average energy in one period.

## Slide 49: Energy and Power - Example
Let us consider the sequence (discrete signal)
It is aperiodic, so we can compute its energy:
Let us now consider the sequence (discrete signal)
It is periodic, so we must compute its power:

## Slide 50
Properties and Visualization
carmine.clemente@strath.ac.uk
Properties and visualization

## Slide 51: Some Signal Properties
Causal Signals
    zero prior to
Periodic Signals
  for some integer N
Random or Aperiodic Signals
No integer N can be found:

## Slide 52: Signal Visualization
Time Plot:
    x[n] versus n
Frequency Plots:
  one-sided Magnitude and Phase Spectra;
  two-sided Magnitude and Phase Spectra.
Time-Frequency Plots:
  Magnitude Spectra versus time on the time- frequency plane

## Slide 53: Signal Visualization
Draw the Time Plot & Frequency plots of a 125Hz Sine wave sampled at fs=1000Hz
One-sided Spectrum of x[n]

## Slide 54: Signal Visualization
Draw the Time Plot & Frequency plots of a 125Hz Sine wave sampled at fs=1000Hz
Two-sided Spectrum of x[n]
Using Euler to convert to two-sided form
Therefore two-sided Magnitude Spectrum of is at ±
The two-sided Phase Spectrum of is at and at

## Slide 55: Signal Visualization

## Slide 56: Matlab Code
function plot_spectra(nsamp,f,fs)
close all
if nargin == 0
nsamp=1000; f=125; fs=1e3;
end
figure ; n=[0:1:nsamp-1] ; t=n/fs;
faxis=[(-nsamp+1)/2:1:nsamp/2]; faxis_onesided=[0:1:(nsamp-1)/2];
faxis=faxis*fs/nsamp; faxis_onesided=faxis_onesided*fs/nsamp;
x=sin(2*pi*f*t);
subplot(4,1,1); stem(n(1:50),x(1:50))
xlabel('time axis n'); ylabel('amplitude')
title('time plot of 125 Hz sinusoidal signal sampled at 1kHz');grid
subplot(4,1,2); ft=fft(x)/nsamp; ft2=fftshift(ft);ft1=ft(1:nsamp/2)
plot(faxis,abs(ft2)); grid
title('2-sided magnitude spectrum of x[n]')
xlabel('frequency axis in Hz'); ylabel('magnitude')
subplot(4,1,3)
ang_ft2=angle(ft2);
ang_ft2(abs(ft2) < 0.01) = 0; % used to avoid random phases
plot(faxis,ang_ft2)
title('2-sided-phase spectrum of x[n]')
xlabel('frequency axis in Hz'); ylabel('phase in radians'); grid
subplot(4,1,4)
plot(faxis_onesided,2*abs(ft1)), ylabel('magnitude')
xlabel(' Freq axis f in Hz')
title('one sided magnitude spectrum')
grid

## Slide 57
X THE PLACE OF USEFUL LEARNING