## Slide 1
Digital Filters Design: FIR design methods
carmine.clemente@strath.ac.uk
Digital filters

## Slide 2: Introduction
The design of FIR filters is generally easier than IIR filters;
Also in this case we will introduce 2 methods: Window and Optimal design.
We will also see how we can use Matlab to design a wide range of FIR filters.

## Slide 3: Introduction
The design of FIR filters is generally easier than IIR filters;
Also in this case we will introduce 2 methods: Window and Optimal design.
We will also see how we can use Matlab to design a wide range of FIR filters.

## Slide 4: Windows
Windowing using window functions are used to reduce the effects of Scallop Loss and Spectral Leakage.
First let us define 5 popular windows of length N.
Rectangular
Hanning
Hamming
Blackman
Kaiser
Each window has its own characteristics in terms of Side-lobe levels and main-lobe size.
I0 is the zeroth-order modified Bessel function of the first kind

## Slide 5: Windows
Time plot – N=40

## Slide 6: Windows- Spectra
Lower side lobes mitigate spectral leakage… but the main lobe broadens!

## Slide 7: FIR design using windows
Ideal Specifications of Digital LP Filter with cutoff freqs
if we compute the IDTFT of we obtain the ideal ]

## Slide 8: Impulse response of Ideal LP digital Filter
Impulse response of ideal LP filter
h[n] is infinite! we need to truncate it to make it finite

## Slide 9: Example
Design a causal, FIR LPF with 41 taps (coefficients) with Linear Phase (Symmetric Impulse Response)

## Slide 10: Example
Truncation:
Extract 41 non zero coefficients using a rectangular Window of length 41
w[n] = 1 for -20 < n < 20
= 0 otherwise
i.e. Truncate the infinite duration IR to a Finite Impulse Response (FIR) using a rectangular window

## Slide 11: Example
Truncation:
Now we need to make it causal and we need to mitigate the edge effects due to the truncation

## Slide 12: Example
Make it causal:
Add 20 poles at to make the filter a causal filter (i.e. shift the 1st coefficient from to
starts for , so it is causal!

## Slide 13: Example
Reduce windowing issues (Spectral Leakage): apply another window (e.g. Hamming)
x

## Slide 14: Example
41 taps impulse response

## Slide 15: Example
41 taps impulse response

## Slide 16: Example
41 taps impulse response

## Slide 17: Characteristics of Window based FIR Filters
Window | N(∆B) Hz | As dBs | Sidel Lobe dBs | SL dBs
Rectangular | 0.9 | -21 | -13 | 3.92
Hanning | 3.1 | -44 | -31 | 1.42
Hamming | 3.3 | -53 | -41 | 1.78
Blackman | 5.5 | -74 | -57 | 1.10
Kaiser b=2 | 1.5 | -29 | -19 | 1.46
b=4 | 2.6 | -45 | -30 | 
b=6 | 3.8 | -63 | -44 | 
b=10 | 5.1 | -81 | -59 | 
b=12 | 6.4 | -99 | -74 | 
is the product between number of coefficients and transition bands
is the stopband attenuation

## Slide 18: Optimal FIR Filters design
Design a lowpass filter with a passband-edge frequency of 1500Hz, a stopband-edge of 2000Hz, passband ripple of 0.01, stopband ripple of 0.1, and a sampling frequency of 8000Hz.
Use the Parks-McClellan Optimal method.
With this method we can control the ripple levels (not possible with the windows based approach).

## Slide 19: Parks-McClellan in Matlab
[n,fo,mo,w] = firpmord( [1500 2000], [1 0], [0.01 0.1], 8000 );
n = 21
fo = [0 0.375 0.5 1.0]
mo = [1 1 0 0]
w = [ 10 1]
b = firpm(n,fo,mo,w); % this computes the 22 coefficients of the impulse response of the low pass filter.
Exercise: using help and doc in Matlab understand how these lines of code operate.

## Slide 20: Parks-McClellan in Matlab

## Slide 21: Other ways to design FIR filters In MATLAB
many fir* functions available

## Slide 22: Filter Designer